## Slide 1: Custom Hardware State-Machines and Datapaths – Using LLVM to Generate FPGA Accelerators
Alan Baker
Altera Corporation

## Slide 2: FPGAs are Awesome
Fully Configurable Architecture
Low-Power
Customizable I/O

## Slide 3: FPGA Design Hurdles
Traditional FPGA design entry done in hardware description languages (HDL)
  e.g. Verilog or VHDL
  HDL describe the register transfer level (RTL)
  Programmer is responsible for describing all the hardware and its behaviour in every clock cycle
  The hardware to describe a relatively small program can take months to implement
  Testing is difficult
Far fewer hardware designers than software designers

## Slide 4: Simpler Design Entry
Use a higher level of abstraction
  Easier to describe an algorithm in C than Verilog
  Increases productivity
  Simpler to test and verify
  Increases the size of the developer pool
Sounds promising, but how can we map a higher level language to an FPGA?

## Slide 5: Our Vision
Leverage the software community’s resources
LLVM is a great compiler framework
  Mature
  Robust
  Well architected
  Easy to modify and extend
  Same IR for different input languages
We modify LLVM to generate Verilog
  Implemented a custom backend target

## Slide 6: OpenCL
Our higher level language
Hardware agnostic compute language
  Invented by Apple
  2008 Specification Donated to Khronos Group and Khronos Compute Working Group was formed
What does OpenCL give us?
  Industry standard programming model
  Aimed at heterogeneous compute acceleration
  Functional portability across platforms

## Slide 7: OpenCL Conformance
You must pass conformance to claim OpenCL support
  Over 8000 tests
  Only one FPGA vendor has passed conformance

## Slide 8: The BIG Idea behind OpenCL
OpenCL execution model …
  Define N-dimensional computation domain
  Execute a kernel at each point in computation domain
void trad_mul(int n,
const float *a, const float *b,
float *c) {
int i;
for (i=0; i<n; i++)
c[i] = a[i] * b[i];
}
Traditional loops
kernel void dp_mul(global const float *a,
global const float *b,
global float *c) {
int id = get_global_id(0);
c[id] = a[id] * b[id]; } // execute over “n” work-items
Data Parallel OpenCL
Notes: 8

## Slide 9: FPGAs vs CPUs
FPGAs are dramatically different than CPUs
Massive fine-grained parallelism
Complete configurability
Huge internal bandwidth
No callstack
No dynamic memory allocation
Very different instruction costs
No fixed number of program registers
No fixed memory system

## Slide 10: Targeting an Architecture
In a CPU, the program is mapped to a fixed architecture
In an FPGA, there is NO fixed architecture
The program defines the architecture
Instead of the architecture constraining the program, the program is constrained by the available resources

## Slide 11: Datapath Architecture
FPGA datapath ~ Unrolled CPU hardware

## Slide 12: A simple 3-address CPU
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 13: Load immediate value into register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 14: Load memory value into register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 15: Store register value into memory
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 16: Add two registers, store result in register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 17: Multiply two registers, store result in register
B
A
A
ALU
Op
Val
Instruction
Fetch
Registers
Aaddr
Baddr
Caddr
PC
Load
Store
LdAddr
StAddr
CWriteEnable
C
Op
LdData
StData
Op
CData

## Slide 18: A simple program
Mem[100] += 42 * Mem[101]
CPU instructions:
  R0  Load Mem[100]
  R1  Load Mem[101]
  R2  Load #42
  R2  Mul R1, R2
  R0  Add R2, R0
  Store R0  Mem[100]

## Slide 19: CPU activity, step by step
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A
Time

## Slide 20: Unroll the CPU hardware…
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A
Space

## Slide 21: … and specialize by position
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A
Instructions are fixed. Remove “Fetch”

## Slide 22: … and specialize
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops

## Slide 23: … and specialize
A
A
A
A
A
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
A
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store

## Slide 24: … and specialize
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.

## Slide 25: … and specialize
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.
Remove dead data.
Fundamental Datapath
Instead of a register file, live data is carried through register stages like a pipelined CPU instruction
Live ranges define the amount of data carried at each register stage

## Slide 26: Optimize the Datapath
R0  Load Mem[100]
R1  Load Mem[101]
R2  Load #42
R2  Mul R1, R2
R0  Add R2, R0
Store R0  Mem[100]
Instructions are fixed. Remove “Fetch”
Remove unused ALU ops
Remove unused Load / Store
Wire up registers properly! And propagate state.
Remove dead data.
Reschedule!

## Slide 27
FPGA datapath = Your algorithm, in silicon
Load
Load
Store
42

## Slide 28: Data parallel kernel
__kernel void
sum(__global const float *a,
__global const float *b,
__global float *answer)
{
int xid = get_global_id(0);
answer[xid] = a[xid] + b[xid];
}
float *a =
float *b =
float *answer =
0
1
2
3
4
5
6
7
7
6
5
4
3
2
1
0
7
7
7
7
7
7
7
7
__kernel void sum( … );

## Slide 29: Example Datapath for Vector Add
On each cycle the portions of the datapath are processing different threads
While thread 2 is being loaded, thread 1 is being added, and thread 0 is being stored
Load
Load
Store
0
1
2
3
4
5
6
7
8 work items for vector add example
+
Work item IDs

## Slide 30: Example Datapath for Vector Add
On each cycle the portions of the datapath are processing different threads
While thread 2 is being loaded, thread 1 is being added, and thread 0 is being stored
Load
Load
Store
0
1
2
3
4
5
6
7
8 work items for vector add example
+
Work item IDs

## Slide 31: Example Datapath for Vector Add
On each cycle the portions of the datapath are processing different threads
While thread 2 is being loaded, thread 1 is being added, and thread 0 is being stored
Load
Load
Store
0
1
2
3
4
5
6
7
8 work items for vector add example
+
Work item IDs

## Slide 32: Example Datapath for Vector Add
On each cycle the portions of the datapath are processing different threads
While thread 2 is being loaded, thread 1 is being added, and thread 0 is being stored
Load
Load
Store
1
2
3
4
5
6
7
8 work items for vector add example
+
0
Work item IDs

## Slide 33: Example Datapath for Vector Add
On each cycle the portions of the datapath are processing different threads
While thread 2 is being loaded, thread 1 is being added, and thread 0 is being stored
Load
Load
Store
2
3
4
5
6
7
8 work items for vector add example
+
0
1
Silicon used efficiently at steady-state
Work item IDs

## Slide 34: High Level Datapath Generation
Compiler Flow

## Slide 35: Compiler Flow
AOC
FPGA Programming File
kernel void
sum(global float *a,
global float *b,
global float *c)
{
int gid = get_global_id(0);
c[gid] = a[gid] + b[gid];
}
Source Code
Altera Offline Compiler
LLC
OPT
Clang
Verilog Design File
Frontend
Parses OpenCL extensions and intrinsics to produce LLVM IR
Clang
OPT
Middle end
Clang –O3 optimizations followed by numerous custom passes to target the FPGA architecture
LLC
Backend
Creates and schedules an elastic pipelined datapath and produces Verilog HDL
LLVM IR is used to describe a custom architecture specific to the program

## Slide 36: Dealing with Resource Constraints
Branch Conversion

## Slide 37: Branch Conversion Example
Branch
A: True
B: False
C

## Slide 38: Branch Conversion Example
Determine control flow to conditionally executed basic blocks
Branch
A: True
B: False
C

## Slide 39: Branch Conversion Example
Determine control flow to conditionally executed basic blocks
Predicate instructions
  A is predicated if the branch was false and vice-versa
Branch
A: True
B: False
C

## Slide 40: Branch Conversion Example
Determine control flow to conditionally executed basic blocks
Predicate instructions
  A is predicated if the branch was false and vice-versa
Combine A and B
  Branch is now unconditional
  PHIs in C become select instructions
Branch
C
A/B

## Slide 41: Branch Conversion Example
Determine control flow to conditionally executed basic blocks
Predicate instructions
  A is predicated if the branch was false and vice-versa
Combine A and B
  Branch is now unconditional
  PHIs in C become select instructions
Simplify the CFG
  Merges remaining blocks
All
Logic

## Slide 42: Branch Conversion
Squeezes the majority of the CFG into one basic block
Saves significant amounts of area
Increased instruction count in the basic block does not adversely affect performance

## Slide 43: Improving Performance of Individual Threads
Loop Pipelining

## Slide 44: OpenCL Task
Kernel operates on a single thread
Data for each iteration depends on the previous iteration
Loop carried dependency bottlenecks performance
__kernel void
accumulate(__global float *a,
__global float *b,
int n)
{
for (int i=1; i<n; ++i)
b[i] = b[i-1] + a[i];
}

## Slide 45: Loop Carried Dependencies
Loop-carried dependency: one iteration of the loop depends upon the results of another iteration of the loop
The value of state in iteration 1 depends on the value from iteration 0
Similarly, iteration 2 depends on the value from iteration 1, etc
kernel void state_machine(ulong n)
{
t_state_vector state = initial_state();
for (ulong i=0; i<n; i++) {
state = next_state( state );
unit y = process( state );
// more work…
}
}

## Slide 46: Loop Carried Dependencies
To achieve acceleration, we can pipeline each iteration of a loop containing loop carried dependencies
  Analyze any dependencies between iterations
  Schedule these operations
  Launch the next iteration as soon as possible
At this point, we can launch the next iteration
kernel void state_machine(ulong n)
{
t_state_vector state = initial_state();
for (ulong i=0; i<n; i++) {
state = next_state( state );
unit y = process( state );
// more work…
}
}

## Slide 47: Loop Pipelining Example
No Loop Pipelining
i0
i1
i2
With Loop Pipelining
i0
i1
i2
i3
i4
Looks almost like ND-range thread execution!
Clock Cycles
Clock Cycles
No Overlap of Iterations
Finishes Faster because Iterations
Are Overlapped

## Slide 48: Pipelined Threads vs. Loop Pipelining
So what’s the difference?
Loop Pipelining enables Pipeline Parallelism AND the communication of state information between iterations.
t0
t1
t2
t3
t4
Pipelined threads launch 1 thread per clock cycle in pipelined fashion
i0
i1
i2
i3
i4
Loop dependencies may not be resolved in 1 clock cycle
Pipelined Threads
Loop Pipelining

## Slide 49: Accumulator Datapath
A new iteration can be launched each cycle
Each iteration still takes multiple cycles to complete, but subsequent iterations are not bottlenecked
__kernel void
accumulate(__global float *a,
__global float *b,
int n)
{
for (int i=1; i<n; ++i)
b[i] = b[i-1] + a[i];
}
Load
Store
+

## Slide 50: Accumulator Datapath
A new iteration can be launched each cycle
Each iteration still takes multiple cycles to complete, but subsequent iterations are bottlenecked
__kernel void
accumulate(__global float *a,
__global float *b,
int n)
{
for (int i=1; i<n; ++i)
b[i] = b[i-1] + a[i];
}
Load
Store
+
i=0

## Slide 51: Accumulator Datapath
A new iteration can be launched each cycle
Each iteration still takes multiple cycles to complete, but subsequent iterations are bottlenecked
__kernel void
accumulate(__global float *a,
__global float *b,
int n)
{
for (int i=1; i<n; ++i)
b[i] = b[i-1] + a[i];
}
Load
Store
+
i=0
i=1

## Slide 52: Accumulator Datapath
A new iteration can be launched each cycle
Each iteration still takes multiple cycles to complete, but subsequent iterations are bottlenecked
__kernel void
accumulate(__global float *a,
__global float *b,
int n)
{
for (int i=1; i<n; ++i)
b[i] = b[i-1] + a[i];
}
Load
Store
+
i=0
i=1
i=2

## Slide 53: Dependence Analysis
Has profound effect on Loop Pipelining
  Can lead to difference in performance of more than 100x
Significant effort spent to improve dependence analysis
  Especially loop-carried dependence analysis
Added complex range analysis to help
Uses knowledge of our specialized hardware and programming model
Never good enough!

## Slide 54: LLVM Issues/Wishlist

## Slide 55: LLVM Issues
Intrinsics don’t support structs
  We extended CallInst for our intrinsics
Module pass managers running every analysis on every function when only requesting a single function
On-the-fly pass manager not inheriting analyses
Ran into several scaling problems with LLVM passes
  Often due to significant loop unrolling and inlining
Loop representation
  Well formed loops are extremely important to us
  Some optimizations introduce extra loops
  while(1) with no return is useful to us

## Slide 56: LLVM Wishlist
Conditional preservation of analyses
Windows debug support
Improved dependence analysis

## Slide 58: References
Altera OpenCL Example Designs
  http://www.altera.com/support/examples/opencl/opencl.html
Altera OpenCL Best Practices Guide
  http://www.altera.com/literature/hb/opencl-sdk/aocl_optimization_guide.pdf
Stratix V Overview
  http://www.altera.com/devices/fpga/stratix-fpgas/stratix-v/stxv-index.jsp
Cyclone V Overview
  http://www.altera.com/devices/fpga/cyclone-v-fpgas/cyv-index.jsp
Stratix V ALM
  www.altera.com/literature/hb/stratix-v/stx5_51002.pdf